## Slide 1: Significance in Measurement
Measurements always involve a comparison.
  When you say that a table is 6 feet long, you're really saying that the table is six times longer than an object that is 1 foot long.
  The foot is a unit; you measure the length of the table by comparing it with an object like a yardstick or a tape measure that is a known number of feet long.

## Slide 2: Significance in Measurement
The comparison always involves some uncertainty.
  If the tape measure has marks every foot, and the table falls between the sixth and seventh marks, you can be certain that the table is longer than six feet and less than seven feet.
  To get a better idea of how long the table actually is , though, you will have to read between the scale division marks.
  This is done by estimating the measurement to the nearest one tenth of the space between scale divisions.

## Slide 3: Significance in Measurement
Which of the following best describes the length of the beetle's body in the picture to the left?
Between 0 and 2 in
Between 1 and 2 in
Between 1.5 and 1.6 in
Between 1.54 and 1.56 in
Between 1.546 and 1.547 in

## Slide 4: Significance in Measurement
The correct answer
is . . .
(d), between 1.54 and 1.56 inches

## Slide 5: Significance in Measurement
Measurements are often written as a single number rather than a range.
  The beetle's length in the previous frame was between 1.54 and 1.56 inches long.
  The single number that best represents the measurement is the center of the range, 1.55 inches.
  When you write the measurement as a single number, it's understood that the last figure (the second of the two 5’s in this case) had to be estimated. Consider measuring the length of the same object with two different rulers.

## Slide 6: Significance in Measurement
For each of the rulers, give the correct length measurement for the steel pellet as a single number rather than a range

## Slide 7: Significance in Measurement
For the ruler on the left you should have had . . .
1.4 in
For the ruler on the right, you should have had . . .
1.47 in

## Slide 8: Significance in Measurement
A zero will occur in the last place of a measurement if the measured value falls exactly on a scale division.
  For example, the temperature on the thermometer should be recorded as 30.0°C.
  Reporting the temperature as 30°C would imply that the measurement had been taken on a thermometer with scale marks 100°C apart!

## Slide 9: Significance in Measurement
A temperature of 17.00°C was recorded with one of the three thermometers to the left. Which one was it?
A) the top one
B) the middle one
C) the bottom one
D) either the top one, or the middle one
E) either the middle one, or the bottom one
F) it could have been any of them

## Slide 10: Significance in Measurement
The correct answer is . . .
D
This is the best choice because . . .
  The top thermometer reads to 0.1 so 0.01 can be estimated
  The middle thermometer reads to 0.2 so 0.02 can be estimated
  In both cases, a reading of 17.00 is possible

## Slide 11: Significance in Measurement
Use the bottom of the meniscus (the curved interface between air and liquid) as a point of reference in making measurements of volume in a graduated cylinder, pipet, or buret.
In reading any scale, your line of sight should be perpendicular to the scale to avoid 'parallax' reading errors.

## Slide 12: Significance in Measurement
Determine the volume readings for the two cylinders to the right, assuming each scale is in mL.

## Slide 13: Significance of Measurement
Numbers obtained by counting have no uncertainty unless the count is very large.
  For example, the word 'sesquipedalian' has 14 letters.
  "14 letters" is not a measurement, since that would imply that we were uncertain about the count in the ones place.
  14 is an exact number here.

## Slide 14: Significance in Measurement
Numbers obtained from definitions have no uncertainty unless they have been rounded off.
  For example, a foot is exactly 12 inches. The 12 is not uncertain at all.
  A foot is also exactly 30.48 centimeters from the definition of the centimeter. The 8 in 30.48 is not uncertain at all.
  But if you say 1 foot is 30.5 centimeters, you've rounded off the definition and the rounded digit is uncertain.

## Slide 15: Significance in Measurement
You should have picked choices . . .
1, 2 and 4
Choices 3 and 5 are incorrect because both are counts are very large.
  Recall that very large counts have uncertainty because of inherent flaws in the counting process.

## Slide 16: Significance in Measurement
All of the digits up to and including the estimated digit are called significant digits.
  Consider the following measurements. The estimated digit is in gold:
Measurement Number of Distance Between Markings
Significant Digits on Measuring Device
142.7 g 4 1 g
103 nm 3 10 nm
2.99798 x 108 m 6 0.0001 x 108 m

## Slide 17: Significance in Measurement
  A sample of liquid has a measured volume of 23.01 mL. Assume that the measurement was recorded properly.
  How many significant digits does the measurement have? 1, 2, 3, or 4?
  The correct answer is . . .
  4

## Slide 18: Significance in Measurement
  Suppose the volume measurement was made with a graduated cylinder. How far apart were the scale divisions on the cylinder, in mL? 10 mL, 1 mL, 0.1 mL, or 0.01 mL?
  The correct answer is . . .
  0.1 mL

## Slide 19: Significance in Measurement
  Which of the digits in the measurement is uncertain? The “2,” “3,” “0,” or “1?”
The correct answer is . . .
1

## Slide 20: Significance in Measurement
Usually one can count significant digits simply by counting all of the digits up to and including the estimated digit.
  It's important to realize, however, that the position of the decimal point has nothing to do with the number of significant digits in a measurement.
  For example, you can write a mass measured as 124.1 g as 0.1241 kg.
  Moving the decimal place doesn't change the fact that this measurement has FOUR significant figures.

## Slide 21: Significance in Measurement
Suppose a mass is given as 127 ng.
  That's 0.127 µg, or 0.000127 mg, or 0.000000127 g.
  These are all just different ways of writing the same measurement, and all have the same number of significant digits: THREE.

## Slide 22: Significance in Measurement
If significant digits are all digits up to and including the first estimated digit, why don't those zeros count?
  If they did, you could change the amount of uncertainty in a measurement that significant figures imply simply by changing the units.
    Say you measured 15 mL
      The 10’s place is certain and the 1’s place is estimated so you have 2 significant digits
    If the units to are changed to L, the number is written as 0.015 L
      If the 0’s were significant, then just by rewriting the number with different units, suddenly you’d have 4 significant digits

## Slide 23: Significance in Measurement
  By not counting those leading zeros, you ensure that the measurement has the same number of figures (and the same relative amount of uncertainty) whether you write it as 0.015 L or 15 mL

## Slide 24: Significance in Measurement
Determine the number of significant digits in the following series of numbers:
  0.000341 kg = 0.341 g = 341 mg
  12 µg = 0.000012 g = 0.000000012 kg
  0.01061 Mg = 10.61 kg = 10610 g

## Slide 25: Significance in Measurement
You should have answered as follows:
  3
  2
  4

## Slide 26: Significance in Measurement
How can you avoid counting zeros that serve merely to locate the decimal point as significant figures? Follow this simple procedure:
  Move the decimal point so that it is just to the right of the first nonzero digit, as you would in converting the number to scientific notation.
  Any zeros the decimal point moves past are not significant, unless they are sandwiched between two significant digits.
  All other figures are taken as significant.

## Slide 27: Significance in Measurement
Any zeros that vanish when you convert a measurement to scientific notation were not really significant figures. Consider the following examples:
0.01234 kg
1.234 x 10-2 kg
4 sig figs
Leading zeros (0.01234 kg) just locate the decimal point. They're never significant.

## Slide 28: Significance in Measurement
0.012340 kg
1.2340 x 10-2 kg
5 sig figs
Notice that you didn't have to move the decimal point past the trailing zero (0.012340 kg) so it doesn't vanish and so is considered significant.
0.000011010 m
1.1010 x 10-5 m
5 sig figs
Again, the leading zeros vanish but the trailing zero doesn't.

## Slide 29: Significance in Measurement
0.3100 m
3.100 x 10-1 m
4 sig figs
Once more, the leading zeros vanish but the trailing zero doesn't.
321,010,000 miles
3.2101 x 108 miles
5 sig figs
Ignore commas. Here, the decimal point is moved past the trailing zeros (321,010,000 miles) in the conversion to scientific notation. They vanish and should not be counted as significant. The first zero (321,010,000 miles) is significant, though, because it's wedged between two significant digits.

## Slide 30: Significance in Measurement
84,000 mg
8.4 x 104 mg
2 sig figs
The decimal point moves past the zeros (84,000 mg) in the conversion. They should not be counted as significant.
32.00 ml
3.200 x 101 ml
4 sig figs
The decimal point didn't move past those last two zeros.

## Slide 31: Significance in Measurement
302.120 lbs
3.02120 x 102 lbs
6 sig figs
The decimal point didn't move past the last zero, so it is significant. The decimal point did move past the 0 between the two and the three, but it's wedged between two significant digits, so it's significant as well.
All of the figures in this measurement are significant

## Slide 32: Significance in Measurement
When are zeros significant?
  From the previous slide, you know that whether a zero is significant or not depends on just where it appears.
  Any zero that serves merely to locate the decimal point is not significant.

## Slide 33: Significance in Measurement
All of the possibilities are covered by the following rules:
  1. Zeros sandwiched between two significant digits are always significant.
  1.0001 km 2501 kg 140.009 Mg
  5, 4, 6

## Slide 34: Significance in Measurement
  2. Trailing zeros to the right of the decimal point are always significant.
  3.0 m 12.000 µm 1000.0 µm
2, 5, 5
3. Leading zeros are never significant.
0.0003 m 0.123 µm 0.0010100 µm
1, 3, 5

## Slide 35: Significance in Measurement
4. Trailing zeros that all appear to the LEFT of the decimal point are not assumed to be significant.
3000 m 1230 µm 92,900,000 miles 1, 3, 3

## Slide 36: Significance in Measurement
Rule 4 covers an ambiguous case. If the zero appears at the end of the number but to the left of the decimal point, we really can't tell if it's significant or not. Is it just locating the decimal point or was that digit actually measured?
  For example, the number 3000 m could have 1, 2, 3, or 4 significant figures, depending on whether the measuring instrument was read to the nearest 100, 10, or 1 meters, respectively. You just can't tell from the number alone.
  All you can safely say is that 3000 m has at least 1 significant figure.

## Slide 37: Significance in Measurement
  The writer of the measurement should use scientific notation to remove this ambiguity. For example, if 3000 m was measured to the nearest meter, the measurement should be written as 3.000 x 103 m.

## Slide 38: Significance in Measurement
  How many significant figures are there in each of the following measurements?
    1010.010 g
    32010.0 g
    0.00302040 g
    0.01030 g
    101000 g
    100 g
    7, 6, 6, 4, 3, 1

## Slide 39: Significance in Measurement
Rounding Off
  Often a recorded measurement that contains more than one uncertain digit must be rounded off to the correct number of significant digits.
  For example, if the last 3 figures in 1.5642 g are uncertain, the measurement should be written as 1.56 g, so that only ONE uncertain digit is displayed.

## Slide 40: Significance in Measurement
Rules for rounding off measurements:
  1. All digits to the right of the first uncertain digit have to be eliminated. Look at the first digit that must be eliminated.
  2. If the digit is greater than or equal to 5, round up.
    1.35343 g rounded to 2 figures is 1.4 g.
    1090 g rounded to 2 figures is 1.1 x 103 g.
    2.34954 g rounded to 3 figures is 2.35 g.

## Slide 41: Significance in Measurement
  3. If the digit is less than 5, round down.
    1.35343 g rounded to 4 figures is 1.353 g.
    1090 g rounded to 1 figures is 1 x 103 g.
    2.34954 g rounded to 5 figures is 2.3495 g.
  Try these:
  2.43479 rounded to 3 figures 1,756,243 rounded to 4 figures 9.973451 rounded to 2 figures

## Slide 42: Significance in Measurement
The correct answers are . . .
  2.43
  1.756 x 106
  1.0 x 101

## Slide 43: Significance in Measurement